## Slide 1: Small Radio Telescope (SRT) Refurbishment
Clayton Hanson

## Slide 2: Special Thanks to Mayo High School!

## Slide 3: Karl Jansky – The First Radio Astronomer
Began working for Bell Labs in 1928
Designed and performed observations with the first radio telescope (bottom left).
Used entirely analog sensors and required all measurements be recorded by hand.
He found various sources of interference in his work, including weather related radio signals and what he termed “Star Noise”.

## Slide 4: What is it? Why are we doing this?
There are several uses for a Radio Telescope
  Observations of weather phenomena within our atmosphere
  Observations of radio emissions from celestial objects such as moons, planets or the sun
  General scans of the sky to see the radio wavelength emissions that the Earth receives (top).

## Slide 6: What We Have, What We Don’t
Came with a hexagonal base and mounting system.
Motor/Gear system
  Motor
  Conversion gears
  180° directional gear
Gear Location Sensors
  Reed switch sensor
  Limiting switches
No Control Box!

## Slide 10: What needs to be done: Motor Controller
A series of switches will be implemented to allow for a reversal of the direction of current through the motor.
The HOYMK SSR-25DD takes an input voltage of 3-32 Volts Direct Current and opens a switch that allows up to 25 Amps through at 5-60 Volts
These switches will be controlled by an Arduino microcontroller.
  Each switch the Arduino runs will use a digital pin out on the Arduino and share a common ground.

## Slide 11: Which way must the current flow?

## Slide 14: Reed Switch Sensor
Where am I?
A reed switch sensor is a break in a wire that opens and closes as a magnet passes by.
Digital Read:
  5 Volts = HIGH (TRUE)
  0 Volts = LOW (FALSE)
Digital
Read

## Slide 15: Reed Sensor Reading
Sampled at 10,000 Hz
Signal Period: Approx. 75 ms
  50 ms HIGH
  25 ms LOW
Very clean signal
May eliminate the need to debounce the sensor
Natural variance in the number of pulses counted between the limits: 0°, 180°
  Forward: 2005 ± 15 pulses
  Reverse: 2200 ± 150 pulses

## Slide 16: Communication is Important
Limiting switches prevent the motor from going further than it is capable of going based on the gear mechanics.
Were the gear to go further there is the potential for the equipment to be damaged.
There is a consistent count between switches in the forward direction, but not the reverse.
Active low switches

## Slide 17: What now?
Calibration:
  The motors will need to be calibrated under full load to determine any changes in the pulse/degree ratio
  New sensors must be installed
The rats nest of wires needs to be cleaned up and mounted
A communication protocol will be established between the Raspberry Pi and the Arduino
  Possible protocols include: I2C, Serial connections, or even sensor to pin out TRUE/FALSE communication
An algorithm must be developed to track objects across the sky
A Software Defined Radio (SDR) and radio receiver will be implemented on the dish
A user interface must be created

## Slide 18: Citations
https://www.haystack.mit.edu/edu/undergrad/srt/
https://www.exploreminnesota.com/sports-in-minnesota/6176/rochester-mayo-high-school
https://www.nytimes.com/1998/06/09/nyregion/commemorating-a-discovery-in-radio-astronomy.html
https://www.haystack.mit.edu/index.html
https://en.wikipedia.org/wiki/Karl_Guthe_Jansky
http://www.astro.ucla.edu/~ghezgroup/gc/journey/wavelength.html
https://asd.gsfc.nasa.gov/archive/mwmw/mmw_allsky.html
https://automation-insights.blog/2016/05/04/reed-switches-vs-magnetoresistive-sensors-gmr/
https://playground.arduino.cc/
https://www.raspberrypi.org/
https://oscarliang.com/raspberry-pi-arduino-connected-i2c/
https://www.cv.nrao.edu/~bkent/computing/gridview.html